## Slide 1
MC4 - Introduction to Airborne LiDAR data processing
15 Sep 2023
Ricardo Dal’Agnol da Silva
UCLA / JPL-NASA / CTrees.org
@RicardoDalagnol
ricds@hotmail.com
@ WorCAP 2023

## Slide 2: Short course goal
Give an overview of airborne LiDAR data and processing
  What is LiDAR?
  Why use LiDAR?
  Where to obtain data?
  How to use the data?
    Processing demonstration with R codes in the repository https://github.com/ricds/lidar_class

## Slide 3: Pre-requirements https://github.com/ricds/lidar_class
R, RStudio, download the contents from the GitHub repository and run these lines from the first script “1_lidR_basic_processing.R” to install the packages. It can take a while so run it now : )

## Slide 4: Basics: What is LiDAR?
Light Detection And Ranging
Technology that emits intense, focused beams of light and measures the time it takes for the reflections to be detected by the sensor
Source: NOAA LiDAR 101. 2012.
Active sensor that allows estimating the height of surface objects

## Slide 5: What is LiDAR?
Light Detection And Ranging
Technology that emits intense, focused beams of light and measures the time it takes for the reflections to be detected by the sensor
Known Elevation

## Slide 6: What is LiDAR?
Light Detection And Ranging
Technology that emits intense, focused beams of light and measures the time it takes for the reflections to be detected by the sensor
How much time until the light hit the surface and return?
Distance = (Speed of Light x Time of Flight) / 2

## Slide 7: What is LiDAR?
Light Detection And Ranging
Technology that emits intense, focused beams of light and measures the time it takes for the reflections to be detected by the sensor
Known Elevation
Known Elevation

## Slide 8: What is LiDAR?
Light Detection And Ranging
Technology that emits intense, focused beams of light and measures the time it takes for the reflections to be detected by the sensor
height

## Slide 9: The Point Cloud

## Slide 10: Lidar multiple returns and interaction with objects
Source: NOAA LiDAR 101. 2012.
Clément Mallet, Frédéric Bretar. (2009). Full-waveform topographic lidar: State-of-the-art. ISPRS Journal.

## Slide 11: Applications: Why use LiDAR ?
Source: National Geographic / NEON - https://www.neonscience.org/lidar-basics

## Slide 12: Archeology - Geoglyphs
Finding evidences of human colonization under the forest canopy using airborne LiDAR DTM
50 m
Iriarte, J., Robinson, M., de Souza, J., Damasceno, A., da Silva, F., Nakahara, F., Ranzi, A. and Aragao, L., 2020. Geometry by Design: Contribution of Lidar to the Understanding of Settlement Patterns of the Mound Villages in SW Amazonia. Journal of Computer Applications in Archaeology, 3(1), pp.151–169. DOI: http://doi.org/10.5334/jcaa.45

## Slide 13: 1-km Biomass estimates aided by orbital LiDAR
Saatchi et al. (2011). Benchmark map of forest carbon stocks in tropical regions across three continents. PNAS.

## Slide 14
30-m spatial resolution global forest canopy height map was developed through the integration of the Global Ecosystem Dynamics Investigation (GEDI) lidar forest structure measurements and Landsat analysis-ready data time-series.

## Slide 15: Orbital lidar IceSat-2 – transect example

## Slide 16: GEDI - Global vegetation height

## Slide 17: Fire impacts on biomass
“Even ten years after the ﬁre event, there was no complete recovery of the height and biomass of the burned areas” (Sato et al. 2016)
Sato, L.Y.; Gomes, V.C.F.; Shimabukuro, Y.E.; Keller, M.; Arai, E.; Dos-Santos, M.N.; Brown, I.F.; Aragão, L.E.O.C. Post-Fire Changes in Forest Biomass Retrieved by Airborne LiDAR in Amazonia. Remote Sens. 2016, 8, 839.

## Slide 18: Human modified forests: carbon source or sinks? Application of multi-temporal LiDAR
Moura, Y.M.; Balzter, H.; Galvão, L.S.; Dalagnol, R.; Espírito-Santo, F.; Santos, E.G.; Garcia, M.; Bispo, P.C.; Oliveira, R.C.; Shimabukuro, Y.E. Carbon Dynamics in a Human-Modified Tropical Forest: A Case Study Using Multi-Temporal LiDAR Data. Remote Sens. 2020, 12, 430.

## Slide 19: Detecting individual tree loss from selective logging
Dalagnol, R.; Phillips, O.L.; Gloor, E.; Galvão, L.S.; Wagner, F.H.; Locks, C.J.; Aragão, L.E.O.C. Quantifying Canopy Tree Loss and Gap Recovery in Tropical Forests under Low-Intensity Logging Using VHR Satellite Imagery and Airborne LiDAR. Remote Sens. 2019, 11, 817.
Logged tree

## Slide 20: Spatial & temporal distribution of plant species
Canopy palm trees detection using airborne LiDAR data and deep learning (Dalagnol et al., 2022)
Red = manual
Yellow = automatic
50 meters

## Slide 21: DTM – Microtopography

## Slide 22: TPI – Topographic Position Index (normalized by mean elevation)
De Reu, J., J. Bourgeois, M. Bats, A. Zwertvaegher, V. Gelorini, et al., (2014) Application of the topographic position index to heterogeneous landscapes. Geomorphology, 186:39-49.

## Slide 23: Landforms (TPI + Slope)
Extra info here (quite beautiful images): http://www.jennessent.com/downloads/tpi-poster-tnc_18x22.pdf

## Slide 24: Sao Paulo City – fully covered by lidar in 2017
Follow these links to access:
https://spamlab.github.io/blog/pmsp_lidar_aws/
https://geosampa.prefeitura.sp.gov.br/PaginasPublicas/_SBC.aspx

## Slide 25: Also, Terrestrial Laser Scanning (TLS) with exceptional detail ! Note that LiDAR does not have ‘spatial resolution’ but ‘point density’
https://doi.org/10.1016/j.ophoto.2023.100045

## Slide 26: Terminologies
TLS: Terrestrial Laser Scanning
ALS: Airborne Laser Scanning
Orbital or Spaceborne LiDAR
DLS: Drone Laser Scanning
LAS file
LAZ file (zipped)
Point density (pt per m2 or other area unit)

## Slide 27: Where to obtain airborne LiDAR data in Brazil?
Paisagens sustentáveis https://www.paisagenslidar.cnptia.embrapa.br/webgis/
EBA Project INPE/CCST
Dr. Jean Ometto
900+ transects across Br. Amazon
Several sites with repeated LiDAR

## Slide 28: What are the sources of orbital LiDAR?
IceSat (Ice, Cloud and land Elevation Satellite) GLAS (Geoscience Laser Altimeter System)
  Data from 2003 to 2009
  https://icesat.gsfc.nasa.gov/icesat/glas.php
IceSat-2
  Data from 2018/2019 to today
  https://icesat-2.gsfc.nasa.gov
GEDI (Global Ecosystem Dynamics Investigation) onboard of the ISS (International Space Station)
  Data from 2019 to 2021(planned)
  https://gedi.umd.edu/

## Slide 29: How to use the data? Metrics: Canopy Height Model (CHM)
Source: K. Zhao et al. (2009); Kellner et al. (2019)
Digital Surface Model (DSM)
Digital Terrain Model (DTM)
Canopy Height Model (CHM)
Notes: Canopy and ground elevation from LiDAR remote sensing. Each image is an interpolated surface derived from LiDAR (a) The surface model contains estimates of canopy elevation relative to a reference ellipsoid (i.e., sea level). To calculate vegetation height above ground, laser pulses are classified as ‘vegetation’ or ‘ground’. Ground pulses were interpolated to produce a digital terrain model, which estimates ground elevation (b). Subtraction of the digital terrain model from the canopy surface produces a model of canopy height (c
http://esapubs.org/archive/ecol/E090/233/metadata.htm

## Slide 30: Lidar metrics and products in lidR
Source: lidR paper

## Slide 31: Resources
NEON Lidar tutorials
https://www.neonscience.org/resources/learning-hub/tutorials
lidR handbook and tutorials
https://jean-romain.github.io/lidRbook/
lidR tutorial by T Goodbody 2023
https://tgoodbody.github.io/lidRtutorial/
Cool Videos with LiDAR explanation:
Space Lasers
https://svs.gsfc.nasa.gov/10835
A 3D Forest Map
https://svs.gsfc.nasa.gov/12398
https://coast.noaa.gov/data/digitalcoast/pdf/lidar-101.pdf

## Slide 32: Summary
The LiDAR data is the highest accurate data for height estimate
Data availability from airborne to orbital is increasing every day
Let’s go for the codes
https://github.com/ricds/lidar_class
@RicardoDalagnol
Ricardo Dal’Agnol da Silva
ricds@hotmail.com